## Slide 1: Heterogeneous Architecture Design for Mesh
ECE 8823 – Interconnection Networks Final Presentaion
Presented by: Wan-Chen Yeh
Instructor: Dr. Tushar Krishna

## Slide 2: Outline
Motivation
Proposed Works
  Buffer utilization
  Hot spot Traffic Generation
  Multiple Injection Rates
  Diagonals with 2x bandwidth
Conclusion
Notes: Here is the outline for my presentation. First I will briefly talk about the motivation, then each of the works and its results will be shown in this presentation. Finally I will conclude the presentation by some points.

## Slide 3: Motivation
NoC design with homogeneous architecture
  Ease of implementation, general to all the designs (o)
  Optimization
    Based on different applications
    Hard to have a general design for all the applications (x)
Configurable architecture: Heterogeneous Design!
    How to evaluate?
    What can be configured?
    What can be improved?
Notes: Most of previous NoC design focus on the homogeneous design that every component is the same in the NoC.
However, since the traffic characteristics for the applications running on multiple processors are different, there is no single optimization for all the scenarios.
Therefore, we can have the heterogeneous design by configuring each of the components in NoC to optimize the system in energy and performance.
Here are three questions we can think about before designing the heterogeneous architecture.
The first one is how to evaluate the system to obtain some useful information from the simulators?
And the second question is which elements or parameters in NoC can be configured?
And the last one is what can be improved based on the above questions.

## Slide 4: Average Buffer Utilization - 1
The statistics from gem5
  Overall/average information: latency, packet injected…
  For individual components: routers, memory controllers…
Router buffer statistics:
  No accumulative buffer information  re-allocate the resources?
  We want to know the buffer occupancy of the NoC!
Notes: The first proposed work is to know the average buffer utilization on gem5 simulator.
The statistics from gem5 can be overall or average information, or for individual components such as routers and memory controllers.
For a single router, the buffer information consists of buffer read and write.
However, the read/write information is not accumulative, which can not be used to re-allocate the buffer resources.
Therefore, we would like to know the buffer occupancy of the NoC.

## Slide 5: Average Buffer Utilization - 2
Each router has one counter
Counter is increased by 1 based on whether the VC is working or not
The utilization information can be obtained from stat.txt
The statistics is in unit of (buffers per cycle)
Notes: To implement this feature, each router has a counter.
The counter is increased by one if the VC status is active, which means the corresponding buffer is occupied.
By accumulating the number of occupied buffer during each cycle time, we can average the utilization by dividing the number of running cycles.
And the information will be stored in stat.txt file for each router.
The figure on the right shows the average buffer utilization in the format of heat map. The case is uniform random traffic for an 8 by 8 mesh with a low injection rate.
The values in the routers represent the average buffer utilization, and the unit is buffers per cycle.
The red color means higher buffer utilization, while the green color means lower occupancy.

## Slide 6: Average Buffer Utilization - 3
What we care about  the buffer utilization among different injection rates
Low injection rate
medium
high
Notes: What we are caring about is the utilization status for different injection rates.
Here is the relationship between the injection rate and the latency, and we selected the low, medium, and high injection rates for each traffic patterns to execute the experiments.
And the high injection rate is the point beyond the saturation point.

## Slide 7: Average Buffer Utilization - 4
Uniform Random traffic
During saturation: the highest average utilization is about 16 buffers within a router.
Inj. rate = 0.2
Inj. rate = 0.38
Inj. rate = 0.02
32x
100x
Notes: For this feature, first we are simulating the uniform random, tornado, and bit complement traffic.
Here I only show the results of uniform random traffic.
The injection rates are got from the previous slide.
The left figure has the low injection rate, while the figure on the right is at the injection rate beyond saturation.
We can see that for low and medium injection rate, the relative buffer utilization is similar to each other.
However, the utilization of center routers for medium injection rate is approximately 32 times as in low injection rate.
And for the high injection rate, the center routers have about 16 buffers, which is 100 times as in low injection rate.
Besides, as we can see, the buffer utilization beyond saturation point is not distributed as the lower injection rates, the buffer utilization concentrates more on the center routers.

## Slide 8: Average Buffer Utilization - 5
Brief summary
  Comparing with the number of buffer read/write access, the buffer utilization has accumulative statistics of the buffer, which can be used to re-allocate buffer resources to the routers.
  To demonstrate this approach, some traffic patterns have been executed in this project with different levels of injection rates.
Notes: Here is a brief summary for this implementation:

## Slide 9: Hot Spot Traffic - 1
The characteristics of a traffic pattern are affected by destination distribution
  Network topology
  Task mapping onto the cores
In reality, some of the nodes in NoC may have more message requests, which leads to more congestions
To model such scenario, the hot spot traffic pattern is created on gem5.
  Corner routers are selected as hot spots because it is easier to observe the traffic in mesh
Notes: The next work is to implement hot spot traffic on gem5.
The characteristics of a traffic pattern are affected by many factors, and one of the factors is the destination distribution, which depends on the network topology and the tasks mapping onto the cores for different applications.
In reality, the traffic is not possible to be evenly distributed, instead, some extreme cases may result in hot spot traffic which has some nodes with more message requests than the rest, leading to more congestions.
In this project, the corner routers are chosen to be the hot spots because it is known that the mesh topology has more traffic passing through the center routers and selecting the corners is easier for us to observe the scenario.

## Slide 10: Hot Spot Traffic - 2
The destination node Nd is determined as follows:
  The hot spot selection is performed randomly.
A pre-defined threshold
Notes: Here is the rule I implement the hot spot traffic:
At the traffic generation time, the source node will generate a random number Rx, and if Rx is greater than a predefined threshold
The destination node is determined by the random number Rx and a threshold Rth, if Rx is greater than Rth, the destination node will be chosen from one of the hot spots randomly,
otherwise it is just like the uniform random traffic.

## Slide 11: Hot Spot Traffic - 3
The saturation point for hot spot traffic is much lower than other traffic patterns.
The routing algorithm affects buffer utilization very much.
Notes: Here is the buffer utilization for hot spot traffic.
As we can see, the relative buffer utilization for all injection rate is mostly distributed along the edges,
so the we can expect that the saturation point is much lower than other traffic patterns.
Besides, we can find that there are more buffer occupied in the vertical edges than in horizontal edges.
This is because we are using XY routing, so we know that the routing algorithm affects the buffer utilization very much.

## Slide 12: Hot Spot Traffic - 4
Brief summary
  The hot spot traffic which has never been implemented on gem5 is completed.
  This project demonstrated one of the possible hot spot cases. The location of hot spot and the probability of selection can be changed based on the application requirements.
  With the buffer utilization information of hot spot, the optimization for routing algorithm is possible
Notes: Here is the summary for hot spot traffic pattern:

## Slide 13: Multiple Injection Rates - 1
In gem5, the injection rate for each NoC is the same for all the routers.
In reality, it is possible that the injection rates are different
In this project, the injection rates are different for the four quadrants.
Notes: The third work is to implement multiple injection rate for mesh.
So far in gem5, the setting for injection rate is for all the nodes in NoC.
However in reality, it is possible that the injection rates are different for the nodes.
In this project, different injection rates are applied on each of the quadrants.
The first quadrant is using the original setting from user, and the second quadrant has two times of the injection rate, and so on.

## Slide 14: Multiple Injection Rates - 2
The experiments are executed for low, medium, and high injection rates, with uniform random traffic
The high injection rates make the boundaries between the quadrants obscure

## Slide 15: Diagonals with 2x bandwidth - 1
[1] A. K. Mishra, N. Vijaykrishnan and C. R. Das, "A case for heterogeneous on-chip interconnects for CMPs,” Computer Architecture (ISCA), 2011 38th Annual International Symposium on, San Jose, CA, 2011, pp. 389-399.
Previous work [1] has shown that the diagonal nodes with more buffers and higher bandwidth can improve the performance
In this project, only the link redistribution is implemented to verify the correctness
Notes: The last approach is to have the diagonal nodes with doubled bandwidth.
As we can see from the figure on the right, the red links has doubled bandwidth.

## Slide 16: Diagonals with 2x bandwidth - 2
Implementation:
  To model different bandwidths for the links, we choose to change the latency for each link.
  For the links with 2x bandwidth, we modify the latency of the corresponding link to half of the default value.
Notes: The implementation method for this work is based on changing the latency of the links to model different bandwidth for the links.
Therefore, for the links with twice bandwidth, we modify the latency of the corresponding link to half of the default value.

## Slide 17: Diagonals with 2x bandwidth - 3
The improvement of buffer utilization are calculated by:
  Green: utilization is greatly reduced due to higher bandwidth links
Notes: The experiment shown in this slide is the improvement of this approach.
The values in the heat map is the percentage of improvement in buffer occupancy,
which is obtained by the difference of buffer utilization between the baseline and the proposed work divided by the baseline utilization.
According to the results, we found that the buffer occupancy are reduced for all the routers, and the green router means it saves more buffers than the routers with red color.
We can see that even when high injection rate, there is still improvement for the proposed work.
The saturation point for this approach can be improved in some traffic patterns. The result is shown in my report.

## Slide 18: Diagonals with 2x bandwidth - 4
We get the area and energy per router from DSENT
  The value is divided by the number of buffers per router.
  Then multiply with the total number of buffers we have for an NoC
For the buffer area, it is reduced approximately by 17%, 16%, and 12% for low, medium, and high injection rates, respectively.
12%
16%
17%
Notes: Then we have some analysis regarding the area and energy for the buffers.
The area and read/write energy for a router is obtained from DSENT.
Since we would like to know the energy and area saved from reducing the number of buffers.
We calculated the energy and area per buffer, then multiply with the total number of buffers of an NoC.
The buffer area is improved by 12% to 17%, for different injection rates.

## Slide 19: Diagonals with 2x bandwidth - 5
The buffer read and write energy for high injection rate can reach 17% when low injection rate.
Notes: The buffer read and write energy can be improved by 17% for high injection rate.

## Slide 20: Diagonals with 2x bandwidth - 6
Brief summary:
  The diagonals with 2x bandwidth links is implemented by modeling half of the latency of the corresponding links.
  Even at high injection rate, the average buffer utilization can be reduced by 30% for the diagonal nodes.
Notes: Here is the summary for this work:

## Slide 21: Conclusion
How to evaluate?
  Buffer utilization
What can be configured?
  Hot spot Traffic Generation
  Multiple Injection Rates
  Diagonals with 2x bandwidth
What can be improved?
  Knowing the buffer utilization = Knowing how much area and energy can be saved!
Notes: So let’s go back to the three questions.
The answer to the first question, is the average buffer utilization is established on gem5, so we can know the buffer occupancy for each router in the NoC.
Then what can be configured?
First I implemented the hot spot traffic that making the nodes with different number of requests.
Then the nodes can be injected packets in different probabilities, and the link bandwidth can be different on the diagonal nodes
Finally the answer to the last question is that by knowing the buffer usage for each router, we can re-allocated the resource and save more energy and area for NoC

## Slide 22: Thanks for listening!
Any Question?